## Slide 1
InVEST Sediment Retention Model
Estimate the amount of watershet erosion and sedimentation and its economic impact on hydropower production and water quality
Two Steps:
Biophysical
Valuation

## Slide 2
Biophysical Inputs
Land Use/Land Cover
Vegetation retention, land practice and management
Slope
Digital elevation model, slope threshold
Sediment Retention Model
Erosivity
Based on intensity and kinetic energy of rainfall
Erodibility
Soil detachment and transport potential due to rainfall
Watershed Areas
Main and sub for point of interest and water quality analysis
Reservoir Features
Dead volume, lifetime of reservoir, allowed load
Streams
Used to determine where sediment flows to

## Slide 3
Biophysical Outputs
Potential Soil loss
Calculated from USLE per sub-watershed
Sediment Retention Model
Sediment Exported
Calculated per sub-watershed
Sediment Retained
Calculated per sub-watershed
Used in valuation

## Slide 4
Valuation Inputs
Valuation Outputs
Value of Sediment Removal for Dredging
Value of Sediment Removal for Water Quality
Sediment Retention Model
Watershed Areas
Main and sub for point of interest and water quality analysis
Sediment Exported
From biophysical analysis
Sediment Retained
From biophysical analysis
Sediment Valuation
Reservoir dredging costs

## Slide 5
How Does it Work?
Use the universal soil loss equation to determine potential soil loss
A connectivity model determines how much soil reaches the stream
  Different land cover and practice can retain sediment!
Details in the user’s guide
Follow me to http://www.naturalcapitalproject.org
Bookmark the user’s guide
Sediment retention model

## Slide 6
Universal Soil Loss Equation
Sediment retention model
Variable | Description
A | Long term average annual soil loss
R | Rainfall erosivity
K | Soil erodability
LS | “Slope Length” Factor
C | Conservation Factor
P | Practice Factor

## Slide 7
Connectivity Model
Sediment retention model
Stream
Corn
Forest
Forest
Corn

## Slide 8
Results
Amount of sediment that reaches streams
Economic impact of sedimentation
  Dredging
  Water Quality

## Slide 9
Future Features
Account for dams in removal of downstream sediment
It’ll run faster
Look for this in InVEST 2.3 in the near future

## Slide 10
Do it!
Run the Soil Loss tool first, then Valuation
I’ll do a dry run
Trainers will help you
Your neighbor will help you
Okay to be rowdy
Sediment retention model